## Slide 1: Subnetting
Notes: 1

## Slide 2: Subnetting Concept

## Slide 3
Subnet Concept
Two ways to address a particular house
  Building number, House number (Normal IP address)
  Building number, Floor number, House number (IP address with subnet)
Network id
Host id
Network id
Host id
Subnet id
Notes: 3

## Slide 4
Subnetting
Divide a network into smaller sub-networks with each subnet having its own IP address
  Allow a network to be split into several internal sub-networks, but act like a single network to the outside world
Motivation: Make better use of the IP address space
IP addresses: Two levels of hierarchy; subnetting makes it three
Notes: 4

## Slide 5: Subnetting Example
Consider a network having IP address 200.1.2.0
We want to divide this into two parts, creating two subnets
Analysis: Network belongs to class C

## Slide 6: Subnetting Example
We want to create two subnets
Subnet 1 will have id 02
Subnet 2 will have id 12
IP address length is always 32 bits
For the current example, we have:
  Net id: 24 bits
  Host id: 8 bits
We need one bit for the subnet id: From where to take, and why?

## Slide 7: Subnetting Example
If we take 1 bit from the net ID
  Net id will become 23 bit
  What will be the impact?
  Current net ID is:
  Which bit to take?
    Suppose we take the last bit in the third octet (i.e. 0)
      Now net ID will become 200.1.1 (because last octet will now be of only 7 bits 0000001)
    Suppose we take the first bit in the first octet (i.e. 1)
      Now net ID will become 72.1.1 (because first octet will now be of only 7 bits 1001000)
Conclusion: We cannot touch the net ID
200 | 1 | 2
11001000 | 00000001 | 00000010

## Slide 8: Subnetting Example
Conclusion: We must take one bit from the host id
This bit must be from the leftmost part of the host id
Now, the host id will only have 7 bits
If borrowed bit = 0, then it represents the first subnet
If borrowed bit = 1, then it represents the second subnet

## Slide 9: Resulting Subnets
IP addresses of the two subnets:
200.1.2.00000000 = 200.1.2.0
200.1.2.10000000 = 200.1.2.128

## Slide 10: Subnet 1
Network address of the subnet = 200.1.2.0
Total number of IP Addresses = 27 = 128
Total number of hosts that can be configured = 128 – 2 = 126
Range of IP Addresses = [200.1.2.00000000, 200.1.2.01111111] = [200.1.2.0, 200.1.2.127]
Broadcast Address = 200.1.2.01111111 = 200.1.2.127

## Slide 11: Subnet 2
Network address of the subnet = 200.1.2.128
Total number of IP Addresses = 27 = 128
Total number of hosts that can be configured = 128 – 2 = 126
Range of IP Addresses = [200.1.2.10000000, 200.1.2.11111111] = [200.1.2.128, 200.1.2.255]
Direct Broadcast Address = 200.1.2.11111111 = 200.1.2.255